## Slide 1: Moving Nozzle Head Update (6/4/2020)
Raghav Agarwal

## Slide 2: Overview
Create a nozzle head attachment capable of motion:
  Along the length of the cage
  Upwards and downwards
  Inwards and outwards
These designs move the nozzle in a 2D fashion with the third dimension being an offset from the front plane of the device
  Desired pitch of the jet-cage interface is assumed to be handled by rotating the rotary table of the cage indexing mechanism

## Slide 3: Revolute Arm
Cylindrical coordinates wrt to base frame [b]
“Simple” controls as only variable motions are 3 rotations and 1 linear translation along parallel horizontal axes (reduce number of pitches, twists, etc. to do transformations for)
Can change orientation of jet by revolving joint 3
  Rotating it can make a circular projection onto a plane normal to the jet face)
Top View
Side View

## Slide 4: Revolute Arm: Link Parameters
Joint: i | Link Twist: αi-1 | Link Length: ai-1 | Link Offset: di | Joint Angle: θi
1 | 0 | 0 | 0 | θ1
2 | 0 | L1 | d2 | θ2
3 | 0 | L2 | 0 | θ3
4 | π/2 | 0 | d4 | 0
Base frame is coincident with joint 1 and fixed in its orientation
Joints 1, 2, and 3 are revolute
Joint 4 is prismatic and is end effector
  Constrained to revolution of joint 3
d2 is fixed whereas d4 is variable (prismatic)

## Slide 5: Revolute Arm: Workspace
Cage sits above base frame
Green circles represent the interior and exterior boundaries of the arm’s workspace
Dashed circle represents the possible path of joint 2
Blue circle represents the possible nozzle path wrt joint 2
Nozzle should be able to cover most/all the cage without crossing below midplane of its workspace
CAGE
NOZZLE
BASE
Joint 2
MIDPLANE

## Slide 6: Rail System Inspiration
Cartesian coordinates wrt base frame situated at the front of the frame
Can either have vertical slides as seen in the top picture (3D printer) or horizontal slides as seen in the bottom picture (Three-link PPP manipulator)
https://www.lulzbot.com/store/printers/lulzbot-taz-6
Figure 3.1: Three-link PPP Manipulator from Introduction to Robotics: Mechanics and controls – Fourth Edition by John J Craig